Progress until 20th May

I made use of mediapipe library which offers hand detection models with very good accuracy. Each hand provides 21 landmarks (x,y) of each joints. I made a dataset of those landmarks coordinates corresponding to the required hand gestures for our project. I made a 5-layer deep neural network model with the train accuracy of 97.25% and test accuracy of 97.09% under 1000 epochs. There are 8 hand gestures in total. (up, down, right,left, forward, backward, stop, land)

Problem We faced at 20th May

Freezing of the video feed from tello/PC while providing control commands to the drone. For eg: if I get the video feed from the tello and then send command to takeoff the drone, the video feed freezes providing no further response to the drone. This happened because the video feed and drone control commands compete for the system resources at the same time.

Concept of Threading

Threading involves creating multiple threads within a single process. Each thread represents an independent flow of execution that can perform its own tasks concurrently. Threads share the same memory space, making it easier to share data between them.

Use of Threading in Gesture Controlled Drone

Handle the video frame processing and gesture recognition in the main loop while using a separate thread to read and update the gesture information from global variables. This approach allows for parallel execution of these tasks and can help improve responsiveness.

Also the variables like up/down veloctity, forward/backward velocity etc. are updated in the main loop according to the gestures. This variables are passed to the drone movement thread. To ensure safe access and modification of the shared varibales, I use a synchronization mechanism like lock.
This way the while updating the variables in main loop, thread will not use it for movement and vice-versa.

Dronekit-python

https://dojofordrones.com/drone-programming/

everything we need including mavlink protocol to communicate with ardupilot firmware and the use of dronekit python library to send command for the drone movement.

tobesenttoBiman
I have implemented the hand gesture detection functionality in the tello drone to control its movement. The challenges that I faced are: freezing of the video providing no response to the drone because of the low system resources. To solve that problem, the concept of threading is used where multiple threads are created to handle the video frame and gesture recognition information.